## Slide 1
Pure Vision SLAM Engineering in Edge Computing Embedded Systems Supervisor: Dewei Yi Student: Jian Chen Department of Computing Science | 
Demonstration

## Slide 2: Content
Part 1: Building map
Part 2: Localization
Part 3: Drone delivery
Part 4: Future work - navigation

## Slide 3: Part 1: Building map
Step 1: Start the system and set the parameter localization to false to switch the system to mapping mode.
  Launch turtlebot3 robot
  Launch Stereo Camera
  Launch uoa_robot_drone orin_stereo_vslam
  Launch uoa_robot_drone pc_stereo_vslam
  Run turtlebot3_teleop teleop_keyboard
Step 2: Operate the robot to walk in the real world, and a map of where the robot goes will be built in real time on the big screen.
Notes: 1. Raspberrypi
clear && cd ~/turtlebot3_ws && ros2 launch turtlebot3_bringup robot.launch.py
2. Jetson Orin Nano
2.1. Stereo Camera
clear && cd ~/colcon_ws && ros2 launch zed_wrapper zed_camera.launch.py | tee zed.log
2.2. SLAM node
clear && cd ~/colcon_ws && ros2 launch uoa_robot_drone orin_stereo_vslam.launch.py localization:=false | tee oriin_vslam.log
3. PC
3.1. display nodes
clear && cd ~/ros2_ws && ros2 launch uoa_robot_drone pc_stereo_vslam.launch.py localization:=false | tee pc_vslam.log
3.2. operation node
clear && cd ~/ros2_ws && ros2 run turtlebot3_teleop teleop_keyboard

## Slide 4: Part 2: Localization
Step 1: Restart the system and set the parameter localization to true to switch the system to localization mode.
Step 2: Operate the robot to walk in the real world, and the robot's position on the map will be displayed in real time on the large-screen map.
Notes: 1. Raspberrypi
clear && cd ~/turtlebot3_ws && ros2 launch turtlebot3_bringup robot.launch.py
2. Jetson Orin Nano
2.1. Stereo Camera
clear && cd ~/colcon_ws && ros2 launch zed_wrapper zed_camera.launch.py | tee zed.log
2.2. SLAM node
clear && cd ~/colcon_ws && ros2 launch uoa_robot_drone orin_stereo_vslam.launch.py localization:=true | tee oriin_vslam.log
3. PC
3.1. display nodes
clear && cd ~/ros2_ws && ros2 launch uoa_robot_drone pc_stereo_vslam.launch.py localization:=true | pc_vslam.log
3.2. operation node
clear && cd ~/ros2_ws && ros2 run turtlebot3_teleop teleop_keyboard

## Slide 5: Part 3: Drone delivery
Step 1: Switch the wireless network to 2.4G Hz.
Step 2: Install the drone onto the robot.
Step 3: Restart the system with localization:=true and with_drone:=true.
Step 4: Turn on the drone.
Step 5: Set a destination on the map.
Step 6: When the robot reaches the target location, the drone will take off automatically.
Notes: 1. Raspberrypi
clear && cd ~/turtlebot3_ws && ros2 launch turtlebot3_bringup robot.launch.py
2. Jetson Orin Nano
2.1. Stereo Camera
clear && cd ~/colcon_ws && ros2 launch zed_wrapper zed_camera.launch.py | tee zed.log
2.2. SLAM node
clear && cd ~/colcon_ws && ros2 launch uoa_robot_drone orin_stereo_vslam.launch.py localization:=true | tee oriin_vslam.log
3. PC
3.1. display nodes
clear && cd ~/ros2_ws && ros2 launch uoa_robot_drone pc_stereo_vslam.launch.py localization:=true with_drone:=true | tee pc_vslam.log
3.2. operation node
clear && cd ~/ros2_ws && ros2 run turtlebot3_teleop teleop_keyboard

## Slide 6: Part 4: Future work - navigation
Step 1: Switch the wireless network to 5G Hz.
Step 2: Dismount the drone from the robot.
Step 3: Restart the system with localization:=true.
Step 4: Set a destination on the map.
Step 5: The map shows a global path line from the robot to the destination and a local path line within the field of its view.
Step 6: The robot will go to the destination. (Still needs a lot of debugging.)
Notes: 1. Raspberrypi
clear && cd ~/turtlebot3_ws && ros2 launch turtlebot3_bringup robot.launch.py
2. Jetson Orin Nano
2.1. Stereo Camera
clear && cd ~/colcon_ws && ros2 launch zed_wrapper zed_camera.launch.py | tee zed.log
2.2. SLAM node
clear && cd ~/colcon_ws && ros2 launch uoa_robot_drone orin_stereo_vslam.launch.py localization:=true | tee oriin_vslam.log
3. PC
3.1. display nodes
clear && cd ~/ros2_ws && ros2 launch uoa_robot_drone nav2_navigation.launch.py localization:=true | tee pc_vslam.log
3.2. operation node
clear && cd ~/ros2_ws && ros2 run turtlebot3_teleop teleop_keyboard

## Slide 7: End